## Slide 1: FMECAENGINE a seamless tool to chain migration simulations and perform related sensitivity analysis
Version 0.45
(Windows & Linux i386/x64)
olivier.vitrac@agroparistech.fr
August, 2011

## Slide 2: LICENSE
FMECAengine is developed by Olivier Vitrac, PhD (Institut National de la Recherche Agronomique) and distributed under licence CeCILL-B (compatible GPL) as detailed below.
CeCILL-B FREE SOFTWARE LICENSE AGREEMENT
http://www.cecill.info/licences/Licence_CeCILL-B_V1-en.html
Notice
This Agreement is a Free Software license agreement that is the result of discussions between its authors in order to ensure compliance with the two main principles guiding its drafting:
firstly, compliance with the principles governing the distribution of Free Software: access to source code, broad rights granted to users,
secondly, the election of a governing law, French law, with which it is conformant, both as regards the law of torts and intellectual property law, and the protection that it offers to both authors and holders of the economic rights over software.

## Slide 3: GOALS
FMECAengine implements FMECA concepts (http://en.wikipedia.org/wiki/FMECA) while being compatible with the underlying physics of mass transfer between food packaging and food.
a formalism as an expert system that enables the simulation of various migration scenarios and the coupling with heterogeneous databases, rulebases and knwoledge bases from industry, final users, research laboratory…
Possible scopes: identification of critical steps within a food packaging flow chart (setoff, hot filling, long term storage, household heating…); seeking critical migrants for various designs (e.g. from adhesives, inks); concurrent design of complex food packaging systems (multicomponents, multilayers).

## Slide 4: VERSION HISTORY
Generating migration scenarios (version 0.1)
Simulating chained scenarios (version 0.2)
Sensitivity analysis (version 0.3)
Severity and criticality analysis (version 0.38)
Connecting with physico-chemical databases (version 0.41)
Multiple keys enabled in versions 0.43 and later

## Slide 5: Which kind of problem can be solved ?

## Slide 6: FMECAENGINE architecture
Polymer
Name : PP
Composition : antioxidant
Additive
Name : BHT
PMREF : 46640
CAS : 128-37-0
M : 220
SML : 3
Class : antioxidant
Monomer
Name : propylene
PMREF : 23980
CAS : 115-07-1
M : 42
SML : 60
Class : propylene
Scenarios
Time
lF
li
SML
CP°i
Di
KFPi
FMECAENGINE
Updated scenarios
FMECADB
Simulation 1
.
.
.
Simulation n
Sensitivity
Severity and criticality
On a signe computer or on a cluster of computer

## Slide 7: What is chained simulation ?
Principles : inherited parameters, parental bond
Toy example
Step1
Step2
Step3
Step4
[P1]
[P2]
[P3]
[P4]

## Slide 8: What is migration simulation?
input
output
Result from a
previous simulation
(e.g. time x space concentration field denoted [c]n-1)
Simulated result
(denoted [c]n)
Parameter vector inherited from step k [p]k + sparse modification [δp]n
[p]n= [p]k +[δp]n
to propagate inheritance

## Slide 9: Object/parallel implementation
input/
output/
Input folder(s)
Onput folder including
Output files
Programming within
a spreadsheet (ODS files preferred)
Database(s) available
for future use

## Slide 10: GOAL: solve complex simulation scenarios with simple inheritance operators and sparse parameters
C
A
B
[p]C= [p]A + [p]B +[δp]C
[δp]C
[p]A
[p]B
[c]C=fC([p]C)
C inherits of parameters of A
C inherits of parameters of B
C reuses the output of B (B is the parent of C)
Bold=higher precedence

## Slide 11: TOY EXAMPLE: input table
dependence graph
plotted by FMECAENGINE
INPUT TABLE =OpenOffice worksheet (ODS v. 3)
ORIGINAL TABLE repainted by FMECAENGINE

## Slide 12: TOY EXAMPLE: output table
Results available as links
Simulations without parent are independent.
Line-through values are inherited from their parents.
Links give direct access to plots.
Chaining defined via ancestors

## Slide 13: TOY EXAMPLE: outputs
INPUT TABLE =OpenOffice worksheet (ODS v. 3)
FMECAENGINE
FMECAENGINE
FMECAENGINE
OUTPUT PARETO CHART
OUTPUT KINETIC GRAPH
FMECAENGINE
OUTPUT TABLE =HTML report
FMECAENGINE
SEVERITY CHART
RESULT GRAPH

## Slide 14: SENSIBILITY ANALYSIS
Principles : automatic creation of combinations (Foscale, Kscale)
Illustrative examples

## Slide 15: CASE STUDY simulation chaining to assess cause trees
MIGRATION
Cap
Body
(multilayer)
LONG-TERM STORAGE
(200 days @25°C)
HOT FILLING
(10 min @80°C)
SETOFF
during storage before use
(100 days@25°C)
MICROWAVE HEATING
5 min @100°C

## Slide 16: CORRESPONDING CODING
Geometry
Composition
Physico-chemical properties
Contact conditions
Contact conditions
Contact conditions
Contact conditions
SETOFF
HOT FILLING
STORAGE
HEATING
As most of values are inherited, the table is highly sparse.
Note that negative Bi values code for setoff (periodic boundary conditions).

## Slide 17: SENSITIVITY OF ANALYSIS An example: 3 levels for each first two steps

## Slide 18: PRINCIPLES OF SENSITIVITY OF ANALYSIS 9 levels combinations
11 | 12 | 13
21 | 22 | 23
31 | 32 | 33

## Slide 19: PRINCIPLES OF SENSITIVITY OF ANALYSIS APPLICATION TO SIMULATION CHAINING Mandatory rule = each step must have a single parent
33
23
13
31
21
11
32
22
12

## Slide 20: A FIRST INTUITIVE IMPLEMENTATION: by hands
Relationship defined
with “id” and “parent”
Note the
sparsity of inputs
INTPUT TABLE

## Slide 21: SPARSITY: PARAMETERS ARE MAINLY INHERITED
Reconstructed full table from column “inherit”
OUTPUT TABLE

## Slide 22: RAPID RESULTS ANALYSIS
Contribution
of HotFilling12
Final concentration
value in food
Color proportional to
The concentration in food (jet colormap).
Comparison of all 9 scenarios
concentration profil l in food for all steps
Severity of all 9 scenarios

## Slide 23: COMBINATORICS via FMECAENGINE automation
Step n n+1 n+2
Step n
The perturbation is applied only to step n
and then propagated to dependent steps
(e.g. local change of temperature/time)
The perturbation is applied to all steps n,n+1,n+2,n+3…
(e.g. small/medium/large molecules)

## Slide 24: ADVANCED EXAMPLE INPUT TABLE (automation columns: Foscale, Kscale) All valid Matlab syntaxes are eligible
SETOFF
HOT FILLING
STORAGE
HEATING
1
2
3
Column vector
Column vector
Row vector

## Slide 25: Automatically created nodes are
yellow

## Slide 26: COMBINATORICS: automatic inheritance
OUTPUT TABLE

## Slide 27: ADVANCED EXAMPLE: Results
18 scenarios
(concentration
in food after the last step=OvenHeating)
Kinetic profil for all scenarios

## Slide 28: COMBINATORICS: OMITTING STEPS
AUTOMATION
OUTPUT TABLE

## Slide 29: OMITTING STEPS: FMECAENGINE builds all trees required to assess the effects of all combinations
Dependence
Inheritance

## Slide 30: OMITTING STEPS: Results
Result graph: variation of final migration depending on combination
Kinetic graph: concentration profil in food for all steps (color corresponds to severity of final migration)

## Slide 31: OMITTING STEPS: Results
8 scenarios
(concentration
in food after the last step=OvenHeating)
Final concentration in food for each scenario length
Omitted step HOT FILLING
Omitted step SETOFF
Omitted step STORAGE
Omitted step OVEN HEATING

## Slide 32: COMPLEX ANALYSES WITH OMITTED STEPS A path towards FMECA-based risk assessment
Small/large diffusants
Good/poor chemical affinity

## Slide 33: COMPLEX ANALYSES WITH OMITTED STEPS A path towards FMECA
OUTPUT TABLE

## Slide 34: COMPLEX ANALYSES WITH OMITTED STEPS: Results
24 scenarios
(concentration
in food after the last step=OvenHeating)
Kinetic profils for 24 scenarios

## Slide 35: SEVERITY and CRITICALITY ANALYSIS
Definition of severity
3 rules for risk migration and management  illustrative example

## Slide 36: DEFINITION OF SEVERITY
Consumer
Exposure
mg/kg body weight
× NOEL/TDI
× >NOEL/TDI
ĈF: (Over)estimated concentration
mg/kg food
HAZARDOUS
SAFE FOR ANIMALS
NOAEL
TDI
HAZARDOUS
NOT COMPLIANT
SML
MINOR, MODERATE
CATASTROPHIC
CRITICAL
100
∞
Severity
SAFE FOR HUMANS
CHILDREN
ADULTS
SMLchildren
x 100
x 3
x 60
1 adult = 60 kg
eats 1 kg/day of
packaged food
Thresholds
mg/kg food
33

## Slide 37: THE SELECTED EXAMPLE ILLUSTRATES NON-INTUITIVE GROUND RULES FOR RISK MITIGATION AND MANAGEMENT
RULE 1
The final migration (consequence) in food does not depend on the order of « contamination » steps.
RULE 2
As migration is cumulative, the individual contribution of each step depends on its position in flowchart. An assessment of modal criticality independent of position is obtained by assessing the final migration without the step to evaluate.
RULE 3
The effect of conditional probabilities must be assessed on the final migration.
IMPLEMENTED GROUND RULES

## Slide 38: CASE STUDY
RISK PRIORITIZATION WITH FMECAENGINE
ĈF
severity is assessed
at the end of all steps

## Slide 39: RULE 1: PERMUTING STEPS (involving a contact with food) DOES NOT CHANGE THE FINAL MIGRATION
EXCHANGEABILITY : SAME ĈF
RESPONSABILITY ?

## Slide 40: RULE 1: PERMUTING STEPS† DOES NOT CHANGE THE FINAL MIGRATION
end
begin
†For steps involving a contact with food
Name of last step
Permuted steps
contact time
food contact

## Slide 41: RULE 2: THE MODAL CRITICALITY ASSOCIATED TO ONE OR A COMBINED STEP(S) IS OBTAINED BY OMITTING THE STEP TO ASSESS
ALL STEPS
LESS 1
LESS 2
ĈF (a.u.)
Omitted step HOT FILLING
Omitted step OVEN HEATING
Omitted step SETOFF
Omitted step STORAGE
100
33
SML
ĈF
Severity

## Slide 42: RULE 2: CALCULATION PROCEDURE TO EXTRACT THE SEVERITY OF A SINGLE STEP
Severity of SETOFF
Severity of STORAGE
Chart: 
| HOT FILLING | OVEN HEATING | SETOFF | STORAGE
Severity | 3 | 5 | 53 | 90
Severity(4 steps)-Severity(3 steps)
33
CRITICAL
STEP
CRITICAL
STEP

## Slide 43: RULE 3: RATING COMBINED MODALITIES REQUIRES TO ASSESS THE CUMULATIVE EFFECT OF ALL COMBINATIONS (e.g. excessive storage and heating)
Storage : t and t+
Oven Heating : D and D+
t
D
D+
t+
additional
modalities
generated by
FMECAENGINE
Missing values
are inherited

## Slide 44: RULE 3: RATING COMBINED EFFECTS here:tD < tD+< t+D < t+D+
TO BE WEIGHTED BY EXPERTS
t
t+
D
D+
D
D+

## Slide 45: RULE 3: MODAL CRITICALITY ASSOCIATED TO [t,D] × [t+,D+]  all sequences with omitted steps (1..3) are tested (43 simulations !).
TREE RESULTS
TREE INHERITANCE BETWEEN TESTED CONDITIONS
NAMES OF LAST STEP
NAMES
OF LAST STEP

## Slide 46: RULE 3: MODAL CRITICALITY ASSOCIATED TO [t,D] × [t+,D+]  all sequences with omitted steps (1..3) are tested (43 simulations).
Severity(4 steps)-Severity(3 steps)
t+D+
t+D
t
D+
t,D
t+,D+

## Slide 47: RATING SEVERITY for a broad range of conditions
Severity of “storage” depends on context.
Increasing criticality
catastrophic
critical

## Slide 48: HOW DOES IT WORK?
Acceptable
region
CF (substance 2)
CF (substance 1)
SML2
SML1
2
1
3
1
2
3
CF(substance1)+CF(substance2)
<Overall migration limit

## Slide 49: APPLICATION: CONCURRENT DESIGN/SCREENING
DESIGN B
DESIGN A
?
?
Identification of
critical components
critical steps
uncorrectable design areas
Feed results into
Design
Quality management procedures
Suppliers audit
Considering related decisions

## Slide 50: COMPLEX EXAMPLE OF COMBINED EFFECTS
200
350
600
M (g/mol)
Fatty contact
Aqueous contact
CF scale

## Slide 51: RATING SEVERITY for several migrants
200
350
600
M (g/mol)
Severity scale
100
33

## Slide 52: RISK BALANCING between migrants
CF + CF ≤ min (SML , SML )
Setoff
Hot filling
Storage
Oven heating
SML
SML
Severity scale
100
33
Fatty contact
Aqueous contact

## Slide 53: Connecting with physico-chemical databases
Relational databases
Key examples (coding with fmecaengine V 0.41 and later)

## Slide 54: RELATIONAL DATABASES
Database = collection of tables including primary, super key and foreign keys
Examples
Additive
name PMREF CAS M SML Class
Monomer
Name C_name PMREF CAS M SML polymer class
Polymer
name composition
Affinity
food K

## Slide 55: IMPLEMENTED RELATIONSHIPS
Implemented relationships include:
  one-to-one relationships
  one-to-many relationships
  many-to-many relationships
  cascading between keys
Operations above are coded using a special syntax (more flexible and concise than SQL) that mimics UML (http://en.wikipedia.org/wiki/Unified_Modeling_Language) :
PP:polymer::name->classadditives
PP:polymer::name->classadditives:substance::class->name
PP:polymer::name->classadditives:substance::class->M
By default, a UNIQUE operator operator (data reduction) is apply to all relationships involving strings or cell array of strings. The request order is respected only for single requests.
It is worth to notice that final results are also included within a large database that can be resused in future simulations or in subsequent analysis (e.g. for calculating severity).
Background:
http://en.wikipedia.org/wiki/Many-to-many_(data_model)
http://en.wikipedia.org/wiki/Junction_table
http://en.wikipedia.org/wiki/Foreign_key
http://en.wikipedia.org/wiki/Superkey
http://en.wikipedia.org/wiki/Associative_Entities

## Slide 56: EXAMPLE OF ONE TO MANY RELATIONSHIPS The example depicts how databases could be used to derive the formulation (substance content) of a common polymer and finally to sample the distribution of molecular mass (M) of possible migrants. These values are finally used for the calculation of some estimates of diffusion coefficients (D).
Data operations (aggregation, reduction, calculation)
Relation between databases
Additive
name PMREF CAS M SML Class
Polymer
name Composition
name | My polymer
composition | 
composition | 
M | value
M | value
M | value
concatenate
request
Previous request
sampling
Destimate
min, max, mean,
median, percentile…

## Slide 57: TIP: the name of a substance can be replaced by a class of substance
name | PP
 | monomer9
 | antioxidant
M | value
request
 | UV_stabilizer
M | value
M | value
M | value
M | value
M | value
M | value
PERCENTILES
0,10, 20…100
100
50
%
M

## Slide 58: RELATIONSHIPS are called KEY or KEY-to-KEY KEY2KEY syntax
Basic coding
keyA:tableA::columnA1->columnA2
keyA:tableA::columnA1->columnA2:tableB::columnB1->columnB2
keyA:tableA::columnA1->columnA2:tableB::columnB1->columnB2:tableC::columnC1->columnC2
Extended coding with mathematical operators
max(Dpiringer(PP,PP:polymer::name->classadditives:substance::class->M,40))
Dpiringer(PP,min(PP:polymer::name->classadditives:substance::class->M),40)
Extended coding with regular expressions
\antiUV{3|2}\ :substance::name->M
\.#PE.#\:polymer::name->classadditives:substance::class->name:substance::name->M
Extended coding with lists
LDPE|undefined|PP:polymer::name->classadditives:substance::class->name:substance::name->M

## Slide 59: EXAMPLES
Collection of K
dairy:affinity::foodK  Kmin, Kmed, Kmax
Any valid Matlab expressions can be accepted
Collection of SML
mean(PP:polymer::namecomposition:additive::classSML)  SMLmean
Collection of D
Dpiringer(PP,PP:polymer::namecomposition:additive::classM,25)  Dmin, Dmed, Dmax
Dpiringer(PP,min(PP:polymer::namecomposition:additive::classM,25))
ou Dmax
max(Dpiringer(PP,PP:polymer::namecomposition:additive::classM,25) )

## Slide 60: EXAMPLE with multiple keys note that all keys must be enclosed within ()
Dpiringer((LDPEYogurtBottle:scenario::id->polymer),
(LDPEYogurtBottle:scenario::id->polymer:polymer::acronym->composition:substance::technologicalclass->M),
(LDPEYogurtBottle:scenario::id->temperature:storage::id->temperature))

## Slide 61: HOW TO BUILD USER DATABASES, RULEBASES, KNOWLEDGEBASES
Database, rulebase, knowledgebase = collection of tables including primary, super key and foreign keys

## Slide 62: Examples: Tables of physico-chemical properties
Additive | 
InChIKey:string (U) Name:string CAS:list of strings PMREF:integer M:real SML:real TDI:real logP: real logPmin: real logPmax: real Class:string | NLZUEZXRPGMBCV-UHFFFAOYSA-N 2,6-Di-t-butyl-4-hydroxytoluene;2,6-di-tert-butyl-4-methyl phenol;4-Methyl-2,6-bis(2-methyl-2-propanyl)phenol;4-Methyl-2,6-di-t-butyl-phenol ;4-Methyl-2,6-ditertbutylphenol;BHT;Butylated hydroxytoluene;phenol, 2,6-bis(1,1-dimethylethyl)-4-methyl;2,6-Di-t-butyl-p-cresol 128-37-0;1948-33-0;25377-21-3;50-78-2;62698-56-0;720-39-8;950-56-1;97123-41-6 46640 220.35 3 0.05 5.2 5.32 5.03 Antioxidant
Polymer | 
Acronym:string Name:string Class:string Density:real Composition: list of strings | PP polypropylene PO 0.95;0.92 antioxidant, UV_stablilizer, monomer
ALL DATA TYPES ARE RECOGNIZED IMPLICITELY ACCORDING TO THE FOLLOWING RULES | 
Empty cell Scalar List Unique (U) Primary/Foreign key | = Not A Number Any numeric value String containing “;” or “¦” is enforced for all keys returning an array of strings Any key with string/char content (possibly including some lists)
Monomer | 
InChIKey:string (U) Name:string CAS:list of strings PMREF:integer M:real SML:real TDI:real logP:list of reals Class:string Polymer:string | QQONPFPTGQHPMA-UHFFFAOYSA-N name: propene;1-propene;propylene;methylethene;1-propylene;prop-1-ene 115-07-1;33004-01-2;676-63-1 23980 42.08 60 NaN 1.7 propylene PP

## Slide 63
Foodsimulant | 
Primary key List | Id: ethanol50 K: 0.1
Diffusion | 
Primary key List | InChIKey: NLZUEZXRPGMBCV-UHFFFAOYSA-N M: 220.35 polymer: PP rhoP: 0.95 temperature: 40 D: 4.6E-15;2.7E-16;5E-15
EXAMPLES: RULE BASES AND KNOWLEDGE BASES
Consumption | 
Primary key List/ Foreign key List/ Foreign key List/ Foreign key | Id : hot Temperature: 70 Time: 2 Unit: h
scenario | 
Primary key Foreign key List/Foreign key Foreign key Foreign key Foreign key Foreign key | Id: gobeletPP Food : hotdrink Foodsimulant: fatty, ethanol50 Material : PP Geometry : gobelet Step : consumption Temperature : hot
Food | 
Primary key List/ Foreign key List/ Foreign key List/ Foreign key | Id: hotdrink Shelflife: 2 Shelflifeunit : h rhoF: 1000
Geometry | 
Primary key List/ Foreign key List/ Foreign key List/ Foreign key List/ Foreign key List/ Foreign key | Id: gobelet A: 170 Aunit: cm2 mF: 200 mFunit: g lP : 150 lPunit : µm

## Slide 64: POSSIBLE EXTENSIONS
Positive lists
Physicochemical properties
Spectra databases
NIST
Ncbi
ChemSpider
PubChem
EPA…
AUTOMATIC TOOL TO IMPORT
AUTOMATIC TOOL TO IMPORT
Building of the first substances database
M
SML
TDI
logP
Tboiling
Tmelting
Spectra :
  -UV-V
  -IR
  -RMN
  -Mass
Chromatogram
etc…

## Slide 65: DETAILED MANUAL
All functions can be downloaded at:
https://github.com/ovitrac/FMECAengine